## Slide 1: Purifying Water
Killing Bacteria That
Could Cause Illness

## Slide 2: What would you do if you ran out of safe drinking water during a disaster?
Sources of Water for Purification
  Rainwater
  Streams
  Rivers
Before Purifying
  Let water settle to the bottom of the container.
  Strain water through a clean cloth or paper towel.

## Slide 3: Purifying Water By Boiling
Put water into a clean pot.
Bring to a rolling boil and boil for at least 3 minutes.
Cool water before using unless it is being used for cooking.

## Slide 4: Purifying Water With Bleach
Place one gallon of water into a clean container
Add ¼ teaspoon of unscented household bleach (5.25% Sodium Hypochlorite)
Stir
Wait 30 minutes
There should be a faint odor of bleach. If not repeat the procedure.

## Slide 5
Do Not Drink Any Water That Has Come Into Contact With Flood Water!
IT CANNOT BE PURIFIED!

## Slide 6: Conclusion
Rainwater, streams, and rivers are a good source of water for purification.
Water must be filtered before purifying.
Water can be purified by boiling for 3 minutes.
Water can be purified by adding ¼ teaspoon of bleach to one gallon of water.
Flood waters cannot be purified.